## Slide 1: Observation errors
Niels Bormann
(n.bormann@ecmwf.int)

## Slide 2
Outline of lecture
What are observation errors?
Estimating observation errors
Specification of observation errors in practice
Observation error correlations
Summary

## Slide 3
Outline of lecture
What are observation errors?
Estimating observation errors
Specification of observation errors in practice
Observation error correlations
Summary

## Slide 4: Observation error and the cost function
Every observation has an error vs the truth:
  Systematic error
    Needs to be removed through bias correction (see separate lecture)
  Random error
    Mostly assumed Gaussian; described by observation error covariance “R” in the observation cost function.

## Slide 5: Contributions to observation error
Measurement error
  E.g., instrument noise for satellite radiances
Forward model (observation operator) error
  E.g., radiative transfer error
Representativeness error
  E.g., point measurement vs model representation
Quality control error
  E.g., error due to the cloud detection scheme missing some clouds in clear-sky radiance assimilation

## Slide 6: Situation-dependence of observation error
Observation errors can be situation-dependent, especially through situation-dependence of the forward model error.
Examples:
  Cloud/rain-affected radiances: Representativeness error is much larger in cloudy/rainy regions than in clear-sky regions
  Effect of height assignment error for Atmospheric Motion Vectors:
Wind
Height
Low shear – small wind error due to height assignment error
Strong shear – larger wind error due to height assignment error

## Slide 7: Situation-dependence of observation error
Observation errors can be situation-dependent, especially through situation-dependence of the forward model error.
Examples:
  Cloud/rain-affected radiances: Representativeness error is much larger in cloudy/rainy regions than in clear-sky regions
  Effect of height assignment error for Atmospheric Motion Vectors:

## Slide 8: Observation error and the cost function
The observation error R is a matrix, often specified through the square root of the diagonals (“σO”) and a correlation matrix (which can be the identity matrix).

## Slide 9: Role of the observation error
R and B together determine the weight of an observation in the assimilation.
In the linear case, the minimum of the cost function can be found at xa:
  “Large” observation error → smaller increment, analysis draws less closely to the observations
  “Small” observation error → larger increment, analysis draws more closely to the observations
Increment
Departure, innovation,
“o-b”

## Slide 10: Current observation error specification for satellite data in the ECMWF system
Globally constant, dependent on channel only:
  ATMS, AIRS, MWHS
Globally constant, error correlations are taken into account:
  IASI, CrIS
Globally constant fraction, dependent on impact parameter:
  GPS-RO
Situation dependent:
  AMSU-A: dependent on satellite, channel, and RT-model contribution
  MW imagers, MW humidity sounders in all-sky: dependent on channel and cloud amount
  AMVs: dependent on level and shear (and satellite, channel, height assignment method)

## Slide 11
Outline of lecture
What are observation errors?
Estimating observation errors
Specification of observation errors in practice
Observation error correlations
Summary

## Slide 12: How can we estimate observation errors?
Several methods exist, broadly categorised as:
  Error inventory:
    Based on considering all contributions to the error/uncertainty
  Diagnostics with collocated observations, e.g.:
    Hollingsworth/Lönnberg on collocated observations
    Triple-collocations
  Diagnostics based on output from DA systems, e.g.:
    O-b statistics
    Hollingsworth/Lönnberg
    Desroziers et al 2005
    Methods that rely on an explicit estimate of B
  Adjoint-based methods

## Slide 13: Error inventory
Estimate the error from all uncertainty contributions.
Example: error inventory for IASI
Instrument noise (from data providers)
Radiative transfer error (difficult…)
Spatial representativeness error
Cloud detection error
Total error
(Courtesy Hyoung-Wook Chun,
Reima Eresmaa)

## Slide 14: Error inventory
Estimate the error from all uncertainty contributions.
Example: error inventory for IASI
Very useful to understand error contributions.
How realistic is each estimate?

## Slide 15: How can we estimate observation errors?
Several methods exist, broadly categorised as:
  Error inventory:
    Based on considering all contributions to the error/uncertainty
  Diagnostics with collocated observations, e.g.:
    Hollingsworth/Lönnberg on collocated observations
    Triple-collocations
  Diagnostics based on output from DA systems, e.g.:
    O-b statistics
    Hollingsworth/Lönnberg
    Desroziers et al 2005
    Methods that rely on an explicit estimate of B
  Adjoint-based methods

## Slide 16: Basic departure-based diagnostics
If observation errors and background errors are uncorrelated then:
In this case, statistics of background departures give an upper bound for the true observation error characteristics.
Used as basis for observation error modelling for humidity/cloud-sensitive MW radiances in all-sky system at ECMWF.
E.g., temperature-sounder AMSU-A in the ECMWF system

## Slide 17: Departure-based diagnostics
Standard deviations of o-b give information on observation and background error combined.
Departure-based diagnostics try to separate contributions from background and observation errors by making assumptions (which may or may not be true). Such as:
  Assume we know the background error characteristics → remove B
  Assume a certain structure of the errors → Hollingsworth/Lönnberg
  Assume weights used in the assimilation system are accurate → Desroziers diagnostic
  All diagnostics assume that the error in the observations and background are uncorrelated.

## Slide 18: Observation error diagnostics: Hollingsworth/Loennberg method (I)
Based on a large database of pairs of departures.
Basic assumption:
  Background errors are spatially correlated, whereas observation errors are not.
  This allows to separate the two contributions to the variances of background departures:
Spatially uncorrelated variance
→ Observation error
Spatially correlated variance
→ Background error
Covariance of
O—B [K2]
Distance between
observation pairs [km]

## Slide 19: Observation error diagnostics: Hollingsworth/Loennberg method (II)
Drawback: Not reliable when observation errors are spatially correlated.
Similar methods have been used with differences between two sets of collocated observations:
  Example: AMVs collocated with radiosondes (Bormann et al 2003).
    Radiosonde error assumed spatially uncorrelated.

## Slide 20: Observation error diagnostics: Desroziers diagnostic (I)
Basic assumptions:
  Assimilation process can be adequately described through linear estimation theory.
  Weights used in the assimilation system are consistent with true observation and background errors.
Then the following relationship can be derived:
with (analysis departure)
(background departure)
(see Desroziers et al. 2005, QJRMS)
Consistency diagnostic for the specification of R.

## Slide 21: Observation error diagnostics: Desroziers diagnostic (II)
Very easy to use.
Can be applied iteratively.
Will give the wrong answer if its assumptions are violated (as with any method!).
For real assimilation systems, the applicability of the diagnostic for estimating observation errors is still subject of research.

## Slide 22: Examples of observation error diagnostics: AMSU-A
Spatial covariances of background departures:
(See also Bormann and Bauer 2010)

## Slide 23: Examples of observation error diagnostics: AMSU-A
Diagnostics for σO

## Slide 24: Examples of observation error diagnostics: AMSU-A
Inter-channel error correlations:
Hollingworth/Loennberg
Desroziers

## Slide 25: Examples of observation error diagnostics: AMSU-A
Spatial error correlations:
Channel 5
Channel 7

## Slide 26: Examples of observation error diagnostics: IASI
Diagnostics for σO
Temperature sounding
LW
Window
WV

## Slide 27: Examples: IASI
Inter-channel error correlations:

## Slide 28: Examples: IASI
Inter-channel error correlations:
Humidity
Ozone

## Slide 29: Pitfalls of observation error diagnostics
Observation error diagnostics give useful estimates, but beware of mis-leading results when assumptions are violated:
  Observation and background errors may not be uncorrelated.
    E.g., quality control can introduce such error correlations.
  Assumed background error characteristics or weights used in the assimilation system may not be correct.
Diagnostics do not tell you where the error comes from.
  Additional physical understanding of the error sources may be beneficial → error inventory.

## Slide 30
Outline of lecture
What are observation errors?
Estimating observation errors
Specification of observation errors in practice
Observation error correlations
Summary

## Slide 31: How to specify observation errors in practice?
Observation error diagnostics can provide guidance for observation error specification in DA, including:
  Relative size of observation and background errors:
  Presence of observation error correlations.
But: Observation errors specified in assimilation systems are often simplified:
  Observation error covariance is often assumed to be diagonal or globally constant.
  Assumed observation errors may need adjustments compared to estimated ones.

## Slide 32: Too large assumed observation errors tend to be safer than too small ones. Why?
Consider linear combination of two estimates xb and y:
The error variance of the linear combination is:
α
Error variance of estimate σa2
σo2
σb2
Danger zone: Too small assumed σo will lead to an analysis worse than the background when the (true) σo> σb.
Assuming an inflated σo will never result in deterioration.
Optimal weighting:

## Slide 33
Observation errors:
Specifying an optimised observation error produces an optimal analysis with minimum error.
background error
optimised OBS
error
optimal
analysis
specified OBS
error
analysis
error

## Slide 34: What to do when there are error correlations?
Thinning
  Ie, reduce observation density so that error correlations are not relevant.
Error inflation
  Ie, use diagonal R with larger σO than diagnostics suggest.
Take error correlations into account in the assimilation

## Slide 35: Spatial error correlations and thinning
If the observations have spatial error correlations, but these are neglected in the assimilation system, assimilating these observations too densely can have a negative effect.
Practical solution: Thinning, ie select one observation within a “thinning box”.
Using fewer observations gives better results!
See Liu and Rabier (2003), QJRMS: “Optimal” thinning when r ≈ 0.15-0.2

## Slide 36: Example: AMSU-A
After thinning to 120 km, error diagnostics suggest little correlations…
Inter-channel error correlations:
Spatial error correlations for channel 7:

## Slide 37: Example: AMSU-A
… diagonal R a good approximation.

## Slide 38: Example: AMSU-A
… diagonal R a good approximation.
α
σo2
σb2
Error variance of estimate σa2

## Slide 39: Examples of observation error diagnostics: IASI
Inter-channel error correlations:

## Slide 40: Example: IASI
Very common approach: Assume diagonal R, but with larger σO than diagnostics suggest (“Error inflation”).
Neglecting error correlation with no inflation can result in an analysis that is worse than the background!
Assimilation of IASI degrades upper tropospheric humidity
Assimilation of IASI improves upper tropospheric humidity
Inflation factor for the diagonal values of R
Normalised stdev(o-b) for MHS ch 3

## Slide 41: Example: IASI
Background departure statistics for other observations are a useful indicator to tune observation errors.
Assimilation of IASI degrades upper tropospheric humidity
Assimilation of IASI improves upper tropospheric humidity
Inflation factor for the diagonal values of R
Normalised stdev(o-b) for MHS ch 3

## Slide 42
Outline of lecture
What are observation errors?
Estimating observation errors
Specification of observation errors in practice
Accounting for observation error correlations
Summary

## Slide 43: Accounting for error correlations
Accounting for observation error correlations is an area of active research.
Efficient methods exist if the error correlations are restricted to small groups of observations (e.g., inter-channel error correlations).
  E.g., calculate R-1 (y – H(x)) without explicit inversion of R, by using Cholesky decomposition (algorithm for solving equations of the form Az = b).
  Used operationally for IASI and CrIS at ECMWF (and the Met Office)
Accounting for spatial error correlations is technically more difficult.

## Slide 44: What is the effect of error correlations?
Error in obs 2
Error in obs 1
Error in obs 2
Error in obs 1
Uncorrelated error
Correlated error

## Slide 45: What is the effect of error correlations?
Error in obs 2
Error in obs 1
Error in obs 2
Error in obs 1
Uncorrelated error
Correlated error
Larger
error
Smaller
error
Error correlations can imply very small errors for some error structures – reconditioning of the matrix may be necessary.

## Slide 46: Single IASI spectrum assimilation experiments (I)
Obs-FG departure
(all channels cloud-free)
Error correlation matrix

## Slide 47: Single IASI spectrum assimilation experiments (I)
Obs-FG departure
(all channels cloud-free)
Temperature increment [K]
Humidity increment [g/Kg]
Model level
T
Q
Without correlation
With correlation
Without correlation
With correlation
Model level
500
100
30
5
850
Pressure [hPa]
500
100
30
5
850
Pressure [hPa]
Increment reduced with error correlations taken into account

## Slide 48: Single IASI spectrum assimilation experiments (II)
Obs-FG departure
(all channels considered cloud-free)
Temperature increment [K]
Humidity increment [g/Kg]
Model level
Model level
T
Q
Without correlation
With correlation
Without correlation
With correlation
500
100
30
5
850
Pressure [hPa]
500
100
30
5
850
Pressure [hPa]
Increment increased with error correlations taken into account

## Slide 49: Single IASI spectrum assimilation experiments (II)
Obs-FG departure
(all channels considered cloud-free)
Temperature increment [K]
Humidity increment [g/Kg]
Model level
Model level
T
Q
Without correlation
With correlation
Without correlation
With correlation
500
100
30
5
850
Pressure [hPa]
500
100
30
5
850
Pressure [hPa]
Introducing error correlations will change the weighting of the observations in a situation-dependent way.
Increment increased with error correlations taken into account

## Slide 50: Effect of error correlations on the assimilation of AIRS and IASI
Assimilation of IASI degrades upper tropospheric humidity
Assimilation of IASI improves upper tropospheric humidity
Inflation factor for the diagonal values of R
Normalised stdev(o-b) for MHS ch 3
Normalised stdev(o-b) for MHS ch 3
Inflation factor for the diagonal values of R
With correlations
Without correlations

## Slide 51: Correlated observation errors for IASI at Met Office
Verification v Observations
Verification v Analyses
+0.209/0.302% UKMO NWP Index
+0.241/0.047% UKMO NWP Index
The use of correlated observation errors for IASI was implemented operationally at the Met Office in January 2013, Weston et al 2014.

## Slide 52
Outline of lecture
What are observation errors?
Diagnosing observation errors
Specification of observation errors in practice
Accounting for observation error correlations
Summary

## Slide 53: Summary of main points
Assigned observation and background errors determine how much weight an observation receives in the assimilation.
For satellite data, “true” observation errors are often correlated (spatially, in time, between channels).
Diagnostics on departure statistics from assimilation systems can be used to provide guidance on the setting of observation errors.
Diagonal observation errors are still widely assumed for many observations, and thinning and error inflation are used to counter-act the effects of error correlations.
However, accounting for error correlations has become more common in the last few years.

## Slide 54: Further reading (I)
Bormann and Bauer (2010): Estimates of spatial and inter-channel observation error characteristics for current sounder radiances for NWP, part I: Methods and application to ATOVS data. QJRMS, 136, 1036-1050.
Bormann et al. (2010): Estimates of spatial and inter-channel observation error characteristics for current sounder radiances for NWP, part II: Application to AIRS and IASI. QJRMS, 136, 1051-1063.
Bormann et al (2016): Enhancing the impact of IASI observations through an updated observation-error covariance matrix. QJRMS, 142: 1767–1780.
Desroziers et al. (2005): Diagnosis of observation, background and analysis error statistics in observation space. QJRMS, 131, 3385-3396.
Hollingworth and Loennberg (1986): The statistical structure of short-range forecast errors as determined from radiosonde data. Part I: The wind field. Tellus, 38A, 111-136.

## Slide 55: Further reading (II)
Janjić, T. , Bormann, N. , Bocquet, M. , Carton, J. A., Cohn, S. E., Dance, S. L., Losa, S. N., Nichols, N. K., Potthast, R. , Waller, J. A. and Weston, P. (2017), On the representation error in data assimilation. QJRMS, doi:10.1002/qj.3130
Liu and Rabier (2003): The potential of high-density observations for numerical weather prediction: A study with simulated observations. QJRMS, 129, 3013-3035.
Weston et al (2014): Accounting for correlated error in the assimilation of high-resolution sounder data. Q.J.R. Meteorol. Soc., 140: 2420–2429. doi: 10.1002/qj.2306