## Slide 1: Microwave spectrum – measurement, modelling and information content
Alan Geer
Thanks to: Bill Bell, Peter Bauer

## Slide 2: FSOI of observing systems, February 2019 100% = full operational observing system
Microwave instruments together account for 30% of short-range forecast impact, with “moist” assimilation (WV, cloud, precipitation channels) having slightly more impact than “dry” assimilation (T channels)

## Slide 3: Two microwave talks:
1. Sensitivities, theory, and instrumentation
  The observations, their physical properties, their information content
  Further reading:
    Grant Petty: A first course in atmospheric radiation
    Thomas and Stamnes: Radiative transfer in the atmosphere and ocean
    Rodgers: Inverse methods in atmospheric sounding
2. Applications, all-sky data assimilation, cloud detection
  The inverse problem – getting useful information from the radiances
  Dealing with observations affected by cloud and precipitation
  Further reading:
    ECMWF tech memos, papers
    (Kalnay: Atmospheric modelling, DA and predictability)

## Slide 4: Orientation

## Slide 5
Visible
SEVIRI channel 1
0.56-0.71 μm
Microwave
AMSR-E channel 37v
8108 μm (37 GHz v-pol)
TB [K]
Window channels
24th August 2008 at around 12UTC
Infrared
SEVIRI channel 10
11-13 μm
from Dundee Satellite Receiving Station, © Eumetsat

## Slide 6: Where is the microwave?
Planck function
Solar
T = 6000K
Terrestrial
T = 290K
Normalised radiance
Frequency
Wavelength
10m
10cm
1mm
10μm
0.1μm
Microwave
Radio
Infrared
Ultraviolet
Visible

## Slide 7: How much energy is there?
Solar
T = 6000K
Terrestrial
T = 290K
Planck
Function
Radiance
W m-2 sr-1 Hz-1
Flux
W m-2 Hz-1
Terrestrial
radiance × 6.28 sr
Solar
radiance × 6×10-5 sr
Deep space
T = 2.7K
Deep space
radiance × 6.28 sr
Flux
10-12 W m-2 Hz-1
Frequency [103 THz]
Solar
Terrestrial

## Slide 8: Atmospheric particles and microwave radiation
Size parameter
30 GHz frequency ↔ 10mm wavelength (λ)
Particle type | Size range, r | Size parameter, x | Scattering solution
Cloud droplets | 5 – 50 μm | 0.003 – 0.03 | Rayleigh
Drizzle | ~100 μm | 0.06 | Rayleigh
Rain drop | 0.1 – 3 mm | 0.06 – 1.8 | Mie
Ice crystals | 10 – 100 μm | 0.006 – 0.06 | Rayleigh, DDA
Snow | 1 – 10 mm | 0.6 – 6 | Mie, DDA
Hailstone | ~10 mm | 6 | Mie, DDA

## Slide 9
Visible
SEVIRI channel 1
0.56-0.71 μm
Microwave
AMSR-E channel 37v
8108 μm (37 GHz v-pol)
TB [K]
Window channels
24th August 2008 at around 12UTC
Infrared
SEVIRI channel 10
11-13 μm
from Dundee Satellite Receiving Station, © Eumetsat

## Slide 10: Sensitivities

## Slide 11: Sensor and channel types
Sensor types (to be explained in later section):
  Swath-scanning
  Conical-scanning
Channel types
  Imaging: generally see the surface
    SST, column water and cloud
  Sounding: generally don’t see the surface
    Temperature sounding – Oxygen lines
    Humidity sounding – H2O lines
  The above is best seen as a ‘historical’ view
    Most microwave channels are sensitive to multiple earth system components including cloud and precipitation

## Slide 12: Sensitivities: window (“imager”) channels
Ocean waves, wind, skin temperature
Atmospheric water vapour
Cloud and precipitation
Sea-ice
SSMIS F-17 channel 13 (19 GHz, v)
Observed TB, 3rd December 2014
Land surface temperature, biomass, soil/rock, soil moisture
Snow cover
High altitude
Deep fresh snow

## Slide 13: Brightness temperature (TB)
Radiance that would be produced by black-body radiation of a specified temperature TB (Planck function)
Convert radiance (a non-intuitive quantity) into the “radiant temperature”
In the microwave, we can use Rayleigh-Jeans approximation:
Radiance
Brightness temperature

## Slide 14: Sensitivities: temperature sounding channels
AMSU-A channel 5 radiances: Metop-A satellite, 9pm 25/4 to 9am 26/4/2012
Cross-track scanner
Observed TB [K]
Temperature of approx. lowest 10km of atmosphere
Zenith angle dependence
Surface sensitivity
Deep convection

## Slide 15: AMSU-A clear-sky nadir weighting functions these are approximately fixed, in an oxygen line (a well-mixed gas)
7 0%
6 0%
5 5%
4 19%
3 56%
2 92%
Channel
Transmittance surface to space

## Slide 16: Sensitivities: humidity sounding channels
SSMIS F-17 channel 11 (183±1 GHz)
Conical scanning imager and sounder
Observed TB [K]
Relative humidity variations
Deep convection

## Slide 17: Humidity-sounding weighting functions (clear-sky)
High humidity: weighting function high in troposphere
Low humidity: weighting function lower in troposphere
TB = 230 K (found at approx. 400 hPa)
TB = 265 K (found at approx. 700 hPa)

## Slide 18: Humidity-sounding weighting functions (deep convection)
Strongly scattering layer of large frozen particles
Humidity weighting function: thermal emission from lower in troposphere
TB = 150 K (not anything like an atmospheric temperature)
TB = 265 K (found at approx. 700 hPa)
Deep space radiation: 2.7K
Scattering layer “reflects” upwelling radiation

## Slide 19: Sensitivities: window (“imager”) channels
Ocean waves, wind, skin temperature
Atmospheric water vapour
Cloud and precipitation
Sea-ice
SSMIS F-17 channel 13 (19 GHz, v)
Observed TB, 3rd December 2014
Land surface temperature, biomass, soil/rock, soil moisture
Snow cover
High altitude
Deep fresh snow

## Slide 20: Imaging channel (low frequency) radiative transfer (cloudy-sky)
Ocean surface: radiatively cold (e.g. 90K, Fresnel)
Or land / snow / sea-ice surface (high emissivity, possibly some scattering)
Cloud (and often rain): acts like an emitting gas
T = 280 K
TB = 2.7 K
TB = 240 K
Water vapour: is an emitting gas

## Slide 21: Radiative transfer basics

## Slide 22
H2O Rotation lines
+
Water vapour continuum
O2 Rotation Lines
+
Dry air continuum
The microwave gaseous absorption spectrum
Absorption coefficient
βa [1/km]
Moist
Dry
Moisture sounding:
22 GHz and 183 GHz water vapour lines
Temperature sounding:
60 GHz oxygen line
“Imaging channels” in the windows

## Slide 23: In gases / cloud : Schwarzchild’s equation
Change in radiance per distance
Absorption coefficient
Planck function
Radiance
Gain through thermal emission
Loss through absorption

## Slide 24
Adding scattering
Extinction coefficient
Scattering coefficient
Gain through thermal emission
Loss through extinction
Gain from scattering into the beam

## Slide 25
Optical depth
Change in optical depth including extinction by scattering
Change in optical depth in a non-scattering atmosphere

## Slide 26
This can be complex to solve:
  , the radiance in one direction, depends on radiance from all other directions:
  and all levels depend on each other
The full scattering radiative transfer equation
Scattering phase function
Single scattering albedo
Direction vector
Change in optical depth
Integral over all solid angle

## Slide 27: Simulating scattering from particles: just need to know
Scattering phase function
Extinction coefficient
Single scattering albedo
More on Wednesday…

## Slide 28: Radiation and the earth’s surface Specular reflection
Emission
Direct reflection
Emissivity

## Slide 29: Emissivity physics: oceans
Plane water surface: low emissivity - Fresnel equations
Macro structure: waves, swell – geometric optics
Micro structure, e.g. cm: diffraction from capillary waves
Foam: much higher emissivity than water
Correction for non-specular reflection
NOAA Ocean Explorer

## Slide 30: Ocean surface emission is polarised
TB [K]
10 GHz v-pol
TB [K]
10 GHz h-pol
Ocean TB:
~150 K v-pol
~90 K h-pol

## Slide 31: Sensors

## Slide 32: The AMSU-B in the Met Office library

## Slide 33: The MHS at EUMETSAT

## Slide 34: AMSU: cross track microwave sounder
Aperture: D< 30cm
Purpose: temperature and moisture sounding
AMSU A1
AMSU A2
AMSU B
Channels 3-15
(50-57 GHz, 89 GHz)
Channels 1&2
(23.8 GHz, 31.4 GHz)
Channels 15-20
(89, 150, 3 × 183GHz)

## Slide 35: Fine-scale structure in the 60 GHz oxygen line
Level to TOA transmittance
from Liebe MPM 92 model
Narrow lines ~ several MHz
Increasing pressure
broadening
Typical MW radiometer passband
at 54.4 GHz

## Slide 36: AMSU-A 50-60 GHz temperature channels
Channel positions and bandwidths are based on trade-offs aimed at simultaneously optimising :
  width of the band (wider bands give lower noise)
  flatness of optical depth across the band (narrow weighting functions)

## Slide 37: SSMIS – A conical microwave sounder / imager
60 cm

## Slide 38: GMI: imager, targeting preciptiation
NOAA
NASA / JAXA
Global precipitation mission:
Launched Feb 2014
Precipitation radar at 13 GHz and 36 GHz

## Slide 39: Field of view size and aperture approximate calculations in a diffraction-limited system
Airy disk size:
θ
Wavelength
D
a
Aperture size
Satellite to earth distance
FOV size
x
T-sounder: 50 GHz: λ ≈ 0.006 m
(like AMSU-A) satellite altitude 800 km
aperture 0.3 m
FOV ≈ 40 km
Imager: 20 GHz: λ ≈ 0.016 m
(like GMI) satellite altitude 400 km
45° view angle: a=600 km
aperture 1.2 m
FOV ≈ 20 km

## Slide 40: Frequency allocation and protection
3 KHz
30 GHz
300 GHz
Earth observation
Sky Sports

## Slide 41: What is satellite radiance data assimilation?

## Slide 42
SSMIS F-17 channel 13 (19 GHz, v)
Observed TB, 3rd December 2014
An inverse problem: turn this into initial conditions of wind, temperature, humidity, cloud...

## Slide 43
Satellite radiance data assimilation
Observations
Electromagnetic modelling
Earth system modelling
Data assimilation
Verification
Technical
Obs fits (O-B)
Forecast sens. (FSOI)
Scores
Statistical significance
Atmosphere
Ocean,wave & sea-ice
Land surface
Dynamics
Physics
Satellites
Sensors
Cal/val
New missions
Detective work
Passive
Active
Microwave
Swath
Conical
Cubesats
Infrared
Solar
Space agencies
Frequency protection
Orbital mechanics
Full EM modelling
Geometric optics
Radiative transfer
Fast models
Scattering
Non-scattering
Ocean surface
Water permittivity
Snowpack / sea-ice
Mie theory
Discrete dipole
Lookup tables
Spectroscopy
Particle modelling
Solvers
2-stream
DISORT
Monte-Carlo 3D
Scalar or vector (full Stokes)
Principal components
Surface interactions
Particle interactions
Absorption/ emission
Algorithms
Ensemble
Variational
4D-Var
EDA
Observation errors
Background errors
Quality control
Bias correction
VarQC
BgQC
Thin
VarBC
Instrument noise
Modelling error
Representation error
Correlations
Debugging
Coding
ODB
Supercomputing