## Slide 1: ECMWF/EUMETSAT NWP-SAF Satellite data assimilation Training Course
3-7 April 2017

## Slide 2: Practical Exercises with 1DVAR

## Slide 3: The Background and True profile
Can we push the background profile towards the truth using radiances ?

## Slide 4: Practical Exercises with 1DVAR
from a single AMSU-A channel
from 15 AMSU-A channels
from 800 IASI channels
Can we push the background profile towards the truth using radiances…

## Slide 5
model state
observations
background error
covariance
observation* error
covariance
observation operator
(maps the model state to the observation space)
…when we minimise J(x) …

## Slide 6
Kalman gain x
The state that minimizes the cost function is equivalent to a linear correction of the background using the observations:
…where the correction is the Kalman Gain Matrix multiplied by the innovation vector (observation minus radiances simulated from the background)
...we correct background errors
correction term =
innovation

## Slide 7: How does the 1DVAR simulator work ?
Define a background profile Xb
Define a background error covariance B
Define a set of observations (channels) Y
Define an observation error covariance R
Define a true profile Xt
Simulate observed radiances Y from Xt (adding noise consistent with assumed R)
Compute H (RT model) applied to Xb

## Slide 8: Assumed Background Errors (T)

## Slide 9
Weighting functions for AMSUA and IASI channels

## Slide 10: Assumed Observation error for AMSUA channels

## Slide 11: Assumed Observation error for IASI
15 um
4.2um
6.4 um
3.7 um
0.4K
1.0 K
2.0K

## Slide 12
Start up the RTTOV GUI with
type:
module load rttov/12.1
type:
rttovgui
Class01,trd00, 2tDQohR,

## Slide 13: GUI main control window

## Slide 14: GUI pull down menus

## Slide 15: Open a background profile

## Slide 16: Open a background profile

## Slide 17: Open a background profile

## Slide 18: Open a background profile

## Slide 19: Open a background profile

## Slide 20: Have a quick look at the profile

## Slide 21: Have a quick look at the profile

## Slide 22: Exercise #1 – Using a single AMSUA channel
File/Open Profile to select and Open Background_Profile.h5 from profiles directory (have a quick look at the profile in the Windows/Profile Editor Window)
RTTOV/Load Coefficients to Choose and Open and Load AMSUA RT coefficients rtcoef_metop_2_amsua.dat from coefficients directory
RTTOV/Run RTTOV K to look at weighting functions (use the KP button to look at channel 14)
RTTOV/Select Channels to select channel 14 (peaks ~ 2hPa)
1DVAR/Configure 1DVAR/Open a True Profile to select and Open True_profile_opt1.h5
In 1DVAR algorithm window click RUN 1DVAR retrieval (drag left mouse button to zoom in Retrieved Profile Window, right click to un-zoom)
Play with assumed background error and re-run 1DVAR

## Slide 23: Choose and Load AMSUA (RT) coefficients

## Slide 24: Choosing (RT) coefficients

## Slide 25: Choosing (RT) coefficients

## Slide 26: Choosing (RT) coefficients

## Slide 27: Choosing (RT) coefficients

## Slide 28: Choosing (RT) coefficients

## Slide 29: Loading (RT) coefficients

## Slide 30: Configure the 1DVAR

## Slide 31: Open a true profile

## Slide 32: Open a true profile

## Slide 33: Open a true profile

## Slide 34: Open a true profile

## Slide 35: Open a true profile

## Slide 36: Select Channels

## Slide 37: Select Channels (AMSUA-14)

## Slide 38: Select Channels (AMSUA-14)
Weighting function for AMSUA channel 14
We expect this channel to give information at this altitude

## Slide 39: Run the 1DVAR

## Slide 40: Run the 1DVAR
Why is the change so small ?

## Slide 41: Try inflating background errors (x10)
…and run the 1DVAR again…

## Slide 42: Result of the 1DVAR using 1 channels from AMSUA (ch 14)
But why is there no change
to the background here?
We now have a much better change here

## Slide 43: Exercise #2 –Using multiple AMSUA channels
File/Open Profile to select and Open Background_Profile.h5 from profiles directory
RTTOV/Load Coefficients to Choose and Open and Load AMSUA RT coefficients rtcoef_metop_2_amsua.dat from coefficients directory
RTTOV/Run RTTOV K to look at weighting functions (note the use of all channels gives good vertical coverage through the profile column)
1DVAR/Configure 1DVAR/Open a True Profile to select and Open True_profile_opt1.h5
RUN 1DVAR retrieval (play with the background errors to tune)

## Slide 44: Select Channels (AMSUA)

## Slide 45: Run the 1DVAR

## Slide 46: Result of the 1DVAR using 15 channels from AMSUA
Why is the performance still so bad here?

## Slide 47: Exercise #3 – A multi-channel IASI retrieval
File/Open Profile to select and Open Background_Profile.h5 from profiles directory
RTTOV/Load Coefficients to Choose and Open and Load IASI RT coefficients rtcoef_metop_2_iasi.dat from coefficients directory
RTTOV/Run RTTOV K to look at weighting functions (note the use of all channels gives good vertical coverage through the profile column)
RTTOV/Select Channels to select a channel thinning factor (e.g. 10)
1DVAR/Configure 1DVAR/Open a True Profile to select and Open True_profile_opt2.h5
RUN 1DVAR retrieval (play with the background errors to tune…does this work ?? Try using just different parts of the IASI spectrum)

## Slide 48: Choose and Load (RT) coefficients

## Slide 49: Choosing (RT) coefficients

## Slide 50: Choosing (RT) coefficients

## Slide 51: Choosing (RT) coefficients

## Slide 52: Choosing IASI (RT) coefficients

## Slide 53: Choosing (RT) coefficients

## Slide 54: Loading (RT) coefficients

## Slide 55: Select Channels (IASI) x10 !!!

## Slide 56: Run the 1DVAR

## Slide 57: Result of the 1DVAR for IASI
With 800 IASI channels we get a really good adjustment of the background towards the truth!